## Slide 1: Why bother to learn programming?
Programming is becoming a necessity in most of the sciences. We’ll stick to physical problems in this course
Traditional analytical tools have certain limitations, since although they have enabled us to solve an incredible range of problems, they are mostly restricted to linear systems
And the vast majority of outstanding problems are inherently nonlinear!
Also, spurred by the rising cost of experimentation, computational physics is used to conduct “experiments” in the virtual world through simulations
Computational physics serves as a critical role at the interface between experimental and theoretical physics
Notes: Linear system = linear function satisfying additivity and homogeniety (wave propagation, differentiation, integration)
Nonlinear system = otherwise (pendulum equation, mass-spring)
In order to insure that experiments are designed properly before construction is ever begun, detailed simulations of the apparatus are carried out. This can only be accomplished by understanding the interaction of the experimental device with the physical phenomenon it is meant to measure. Thus, computational physicists must understand not only the physics that is being studied, but also the capabilities and limitations of the experiment intended to make the measurements.

## Slide 2: Start with the basics… what is a computer?
Various definitions:
    a programmable machine that receives input, stores and manipulates data, and provides output in a useful format.
    a machine for performing calculations automatically
    the most useful and most frustrating thing any human being will ever work with
    a very, very expensive punching bag
A definition more applicable to us:
  A set of devices which work under the control of a stored program, automatically accepting and processing data to produce information
Notes: Distinction between data and information

## Slide 3: Elements of a computer system
CPU
Hard Disk
Motherboard
Printer
Sound Card
GPU
Memory - RAM
Display
Speakers
Network

## Slide 4: Elements of a computer system
CPU
Motherboard
Printer
Sound Card
GPU
Memory - RAM
Display
Network
Speakers
Hard Disk

## Slide 5: Elements of a computer system
CPU
Motherboard
Printer
Sound Card
GPU
Memory - RAM
Display
Network
Speakers
Hard Disk

## Slide 6: Elements of a computer system
CPU
Motherboard
Printer
Sound Card
GPU
Memory - RAM
Display
Network
Speakers
Hard Disk

## Slide 7: Elements of a computer system
CPU
Motherboard
Printer
Sound Card
GPU
Memory - RAM
Display
Network
Speakers
Hard Disk

## Slide 8: Four basic elements
Input
  Getting instructions and data into the computer
Process
  The Central Processing Unit (CPU) processes data according to instructions. Actions include arithmetic operations, comparisons and data transfer
Store
  Main memory (RAM) is used to store temporary data and software in use
  Data for future use is stored on backing store (hard disks, DVDs, flash drives)
Output
  Produce outgoing information or to generate hard copies (monitors, printers)

## Slide 9: There are Computers everywhere!

## Slide 10: Some definitions
Computer carry out instructions, a set of which is called a program. It tells the computer’s control unit what to do
A program is written using a computer language
Software is the general term to describe all the programs and data used in computer systems
Hardware is the collective term used to refer to the series of devices making up a computer
Programming is the art/science/magic of writing software. Programs are usually written as text files. Code is the textual representation of programs
A compiler transforms these text files into a form which the CPU can understand and execute
When a program behaves incorrectly, it is said to have a bug. Debugging is the act of removing bugs from a program

## Slide 11: software
There are two basic software types
  System software
  Affects the control and performance of a computer system:
    To make the best use of the hardware
    To provide common functionality
    To provide a simple interface between the user and computer
  Application software
  Written to solve a particular problem
  User application programs
  Application packages

## Slide 12: Operating systems
A set of programs residing in RAM which directs all operations in a computer
Booting up is the process of calling the OS into RAM from disk
It makes it easier to interact with the computer and helps in managing computer resources
Some main functions of an operating system include:
Job Control
Memory management
Disk management
Hardware control
Security
Multitasking
Networking

## Slide 13: How a Computer system works
Let’s have a quick look at

## Slide 14: What does a cpu do?
The CPU is analogous to the brain of a computer. It’s three main functions are to:
  Carry out instructions and tell the rest of the computer system what to do (the Control Unit)
  Perform arithmetic calculations and data manipulation (the Arithmetic and Logic Unit)
  Hold data and instruction which are in current use (Main Memory)
The speed at which a CPU can performs these tasks depends on its clock-rate (eg. 2.4 GHz: 2.4 billion instructions per second)
The current trend is to pack many CPUs on the same chip (due to transistor size limits & the speed of light)

## Slide 15: The von-neumann architecture
Internal memory locations performing specific tasks
Equivalent to a calculator, performing an arithmetic/logical operation on two operands, producing one result
Controls instruction processing, movement of internal CPU data and provides timing and control signals
Data paths between the CPU and memory

## Slide 16: The fetch-decode-execute cycle
CU fetches the next instruction from main memory (program counter determines instruction address)
1

## Slide 17: The fetch-decode-execute cycle
The instruction is decoded into a language that the ALU can understand
2

## Slide 18: The fetch-decode-execute cycle
Any data operands required to execute the instruction are fetched from memory and placed in registers
3

## Slide 19: The fetch-decode-execute cycle
The ALU executes the instruction and places the results in registers or memory
4

## Slide 20: How computers represent data
Revisiting old concepts

## Slide 21: The binary number system
Computers are digital, electronic machines, and thus use binary logic
There are only two allowable states in a binary system:
ON (1) or OFF (0)
The binary number system uses these two digits (1 and 0), called binary digits, or bits
All programs and data are ultimately recognised as patters of 1’s and 0’s
A byte is the number of bits used to represent one character (8)
Memory size is usually measured in bytes:
  Kilobytes: 1024 bytes in 1 KB = 210 bytes
  Megabytes: 1024 KB in 1 MB = 220 bytes
  Gigabytes: 1024 MB in 1 GB = 230 bytes

## Slide 22: Representing numbers
We count in base 10 (the decimal number system)
Tens Units
1 3
+ 9
2 2
The binary system has two digits (0,1) and the place values are units 2’s, 4’s, 8’s, 16’s …
10112 = (1 x 23) + (0 x 22) + (1 x 21) + (1 x 20) = 11
26710 = (2 x 102) + (6 x 101)
+ (7 x 100)
1810: 18 / 2 = 9 remainder 0
9 / 2 = 4 remainder 1
4 / 2 = 2 remainder 0
2 / 2 = 1 remainder 0
1810 = 1 0 0 1 0

## Slide 23: Other number systems
Sometime different number systems are used as shorthand for binary
Octal numbers are base 8
6910: 69 / 8 = 8 remainder 5
8 / 8 = 1 remainder 0
1 / 8 = 0 remainder 1
6910 = 1 0 58
Hexadecimal numbers are base 16. The symbols 0-9 and letters A-F (equivalent to 10-15) are used, and place values increase in powers of 16
9110: 91 / 16 = 5 remainder 11
5 / 16 = 0 remainder 5
9110 = 5 B16